## Slide 1: Addressing The Network – IPv4 2018 S1
Diploma in Infocomm and Security
IT2762 Networking and Communications

## Slide 2: Overview
Anatomy of an IPv4 address
Binary to Decimal and Decimal to Binary Conversion
3 Types of IPv4 Addresses
Calculate Network, Hosts and Broadcast Addresses
Subnetting with FLSM
Subnetting with VLSM

## Slide 3: The Anatomy of an IPv4 Address
192 . 168 . 10 . 1
11000000 . 10101000 . 00001010 . 00000001
assuming a network mask of 255.255.255.0
an octet
network portion
host portion

## Slide 4: Binary to Decimal Conversion
The Base 10 number system
  245 is actually:
The Binary number system (or Base 2)
  only two digits: 0 and 1
  let’s examine 1 octet, 1 1 1 0 0 1 0 1:-
  Thus 11100101 = 128 + 64 + 32 + 4 + 1
  = 229
1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
x 27 | x 26 | x 25 | x 24 | x 23 | x 22 | x 21 | x 20
128 + | 64 + | 32 + | 0 + | 0 + | 4 + | 0 + | 1
2 | 4 | 5
x 102 | x 101 | x 100
200 + | 40 + | 5
Base 10

## Slide 5: Binary to Decimal Conversion
To simplify conversion, these are the individual values across an octet:-
128 64 32 16 8 4 2 1
Try converting these binary numbers:-
i. 00010001 =
ii. 10010010 =
iii. 11001100 =
iv. 01100110 =
v. 00011110 =
17
146
204
102
30

## Slide 6: Binary to Decimal Conversion
128 64 32 16 8 4 2 1
My personal tips:-
- An octet which consists of 0s followed by all 1s, has the value before the last 0 occurrence:-
Example:
0001 1111, look at the 3rd 0 which is 32. This octet is 31.
0000 0111, look at the 5th 0 which is 8. This octet is 7.
- Octets with only one occurrence of 0, use 255 - (value of the 0 occurrence):-
Example:
1011 1111, value of 0 occurrence is 64, octet = 255 – 64 = 191
1111 0111, value of 0 occurrence is 8, octet = 255 - 8 = 247

## Slide 7: Binary to Decimal Conversion
128 64 32 16 8 4 2 1
- Subnet masks are always 1s followed by 0s. I remember these numbers by heart:-
10000000 = 128
11000000 = 192 (128 + 64)
11100000 = 224 (128 + 64 +32)
11110000 = 240 (128 + 64 + 32 + 16)
11111000 = 248 (128 + 64 + 32 + 16 + 8)
11111100 = 252 (128 + 64 + 32 + 16 + 8 + 4)

## Slide 8: Binary to Decimal Conversion
128 64 32 16 8 4 2 1
Now try an IP address:-
10101100 . 00010000 . 00110000 . 00010100
More practice at Section 6.1.3.
172.16.48.20

## Slide 9: Decimal to Binary Conversion
128 64 32 16 8 4 2 1
Beginning from the left, find the first positional value that is SMALLER THAN or EQUAL to what you want to convert
Subtract the current value from the positional value and move to the next bit to compare again
Example: convert 35 to binary
  At bit 8, compare 35 with the positional value of 128. Since it is smaller, set bit 8 to 0
  At bit 7, 35 is still smaller than 64. So bit 7 is 0
  At bit 6, 35 is bigger than 32. So bit 6 is 1. Remainder is 35 – 32 = 3
  At bit 5, 3 is smaller than 16. So bit 5 is 0
  At bit 4, 3 is smaller than 8. So bit 4 is 0
  At bit 3, 3 is smaller than 4. So bit 3 is 0
  At bit 2, 3 is bigger than 2. So bit 2 is 1. Remainer is 3 – 2 = 1
  At bit 1, 1 is equal to 1. So bit 1 is 1.
  So 35 in binary is 00100011.

## Slide 10: Decimal to Binary Conversions
128 64 32 16 8 4 2 1
Try converting these decimals to binary:-
i. 16 =
ii. 30 =
iii. 63 =
iv. 172 =
v. 224 =
vi. 252 =
0001 0000
0001 1110
0011 1111
1010 1100
1110 0000
1111 1100

## Slide 11: Binary to Decimal Conversation
128 64 32 16 8 4 2 1
Now try an IP address:-
192.168.100.3
More practice at Section 6.1.5.
11000000.10101000.01100100.00000011

## Slide 12
Types of IPv4 Addresses

## Slide 13: Types of Addresses in an IPv4 Network
In the IPv4 network, there are 3 types of addresses:
Network address
  The address that refers to the particular network
Broadcast address
  A special address used to send data to all hosts in the particular network
Host addresses
  The usable addresses that are assigned to the end devices in the particular network

## Slide 14: Types of Addresses in an IPv4 Network
Network Addresses
  Examples: 10.0.0.0 / 8
172.16.0.0 / 16
192.168.1.128 / 26
The network address is the first address for that network and is used to represent that network
The bits in the host portion of a network address are all 0s
From a network address, the usable host addresses and the broadcast address can be calculated
network prefix

## Slide 15: Types of Addresses in an IPv4 Network
Broadcast Address
  Is a special address for communication to all hosts in that network
  It is the last (or highest) address in the that network
  The bits in the host portion of a network address are all 1s
  Example: for network 192.168.1.0 / 24, the broadcast address would be 192.168.1.255
Host Addresses
  These are the addresses between the network address and the broadcast address
  These are the usable addresses assigned to devices
Network Address | Usable Addresses | Broadcast Address
192.168.1.0 /24 | 192.168.1.1 – 192.168.1.254 | 192.168.1.255

## Slide 16
Calculating Addresses

## Slide 17: IPv4 Network: Network Prefixes
The network prefix is the number of bits that represents the network portion of the address.
The remainder of the network address represents the host bits.
Example:
172.16.4.0 /24
  The first 24 bits represents the network portion
  The remaining 8 bits represents the host portion
A different prefix would change the host range and broadcast address for each subnet

## Slide 18: Calculating Network, Hosts, and Broadcast Address
Given an IP address: 172.16.20.140 /25
To calculate Network Address for this network:
Set the bits in the host portion to “0”
  The prefix “/25” shows that the network portion ends on the 25th bit
  Thus, the host portion starts on the 26th to the 32nd bit
  Bit 25 falls within the 4th octet
  Convert the 4th octet value, 140 to binary and mark the separation:
  Setting the host bits to 0 makes it 10000000, which is 128
  Thus, the network address is 172.16.20.128 /25
  We’ll use this network address in the next slide
network
host
1 0001100

## Slide 19: Calculating Network, Hosts, and Broadcast Address
Continuing with the IP address: 172.16.20.140 /25
To calculate the First Host Address:
This is always one greater than the network address
  From the network address, set only the last host bit to “1” (10000001)
  Thus, the first (lowest) host address is 172.16.20.129

## Slide 20: Calculating Network, Hosts, and Broadcast Address
Continuing with the IP address: 172.16.20.140 /25
Broadcast Address
Set the host portion bits to “1”
  Setting all the host bits to 1 makes it 11111111, which is 255
  Thus, the broadcast address is 172.16.20.255
Last Host Address:
This is always one less than the broadcast address
  From the broadcast address, set only the last host bit to “0” (11111110)
  Thus, the last (highest) host address is 172.16.20.254
network
host
1 0001100
140 in binary

## Slide 21: Calculating Network, Hosts, and Broadcast Address
Thus for the IP address 172.16.20.140 /25
Try this: 10.10.20.4 /20
  Network address:
  1st address:
  Last address:
  Broadcast address:
More practice at Section 6.2.2.
Network Addr. | Usable Addr. | Broadcast Addr.
172.16.20.128 /25 | 172.16.20.129 – 172.16.20.254 | 172.16.20.255
10.10.16.0 /20
10.10.16.1
10.10.31.254
10.10.31.255

## Slide 22: Questions
What kind of address is 10.0.2.192 /26?
  ANS: network address
Does 172.20.1.130 belong to network 172.20.1.0 /25?
  ANS: No, the last usable address for network 172.20.1.0 /25 is 172.20.1.126
What is the 1st usable address for the network that has IP address 10.20.0.10 /12?
  ANS: by setting host bits to 0 to find the network address, the following address will be the 1st usable address, which is 10.16.0.1.

## Slide 23: Subnetting
FLSM subnetting
VLSM subnetting

## Slide 24: Basic Subnetting
Subnetting allows you to create multiple logical networks to exist within a single address block
Unrealistic to use a single network
without subnets. Why?
Given a network address block and prefix, how can we subnet it?
  We “borrow” bits from the host portion
  The “borrowed” bits goes into the network portion and the host portion becomes smaller
Notes: Breaking up a network increases network performance
  End devices broadcasting in a single large network can decrease network performance
Security purposes
Segregating by functions / depts

## Slide 25
To illustrate, using network address block 192.168.10.0 /24
If we borrow 2 bits from the host portion, the subnet address becomes:-
    192.168.10.0 /26 (/26 is subnet mask 255.255.255.192)
In binary form, we shifted the separator 2 bits into the host portion
192.168.10.0
network host
11000000.10101000.00001010.00000000
network host
Basic Subnetting

## Slide 26
Basic Subnetting
We can name the first subnet as subnet 0
From the subnet address of subnet 0, we can calculate:-
  the usable IP address range
  the broadcast address
From here, we move on to calculate the subsequent subnets:-
  Subnet 1
  Subnet 2
  Subnet 3

## Slide 27: Basic Subnetting
So how many bits should we “borrow”?
  It depends on how many subnets we want to create
  # of subnets = 2n where n is the number of bits borrowed
Example: given a network address block 192.168.10.0 /24
  To create 2 subnets, n = 1
    borrow 1 bit (subnet prefix /25)
  To create 4 subnets, n = 2
    borrow 2 bits (subnet prefix /26)
  To create 6 subnets, NOT POSSIBLE
  To create 8 subnets, n = 3
    borrow 3 bits (subnet prefix /27)
Notes: 2 subnets, borrow 1 bit (subnet prefix /25)
4 subnets, borrow 2 bits (subnet prefix /26)
8 subnets, borrow 3 bits (subnet prefix /27)
16 subnets, borrow 4 bits (subnet prefix /28)
32 subnets, borrow 5 bits (subnet prefix /29)

## Slide 28: Basic Subnetting
How many usable host addresses are there in each subnet?
  # of usable addresses = 2h - 2 where h is the # of hosts bits
  Why “- 2”?
Example: using the network address block 192.168.10.0 /24
  If we borrowing 1 bit to create 2 subnets,
    subnet 0 address: 192.168.10.0/25
      # of host bits = 32 – 25 = 7
      # of host addresses = 27 – 2 = 126
  If we borrow 2 bits to create 4 subnets
    subnet 0 address: 192.168.10.0/26
      # of host bits = 32 – 26 = 6
      # of host addresses = 26 – 2 = 62

## Slide 29: Basic Subnetting (2 subnets)
RouterA has two interfaces to interconnect two networks
Given an addr. block 192.168.1.0 /24, let’s create 2 subnets
We borrow one bit from the host portion
  The subnet prefix becomes /25 for each subnet
  The subnet mask in decimal is 255.255.255.128
Thus the subnet information is:-
Subnet | Subnet addr | Usable addr range | Broadcast addr
0 | 192.168.1.0 /25 | 192.168.1.1 - 192.168.1.126 | 192.168.1.127
1 | 192.168.1.128 /25 | 192.168.1.129 - 192.168.1.254 | 192.168.1.255
Notes: Subnet 0, usable address range 192.168.1.1 – 192.168.1.126
Subnet 1, usable address range 192.168.1.129 – 192.168.1.254

## Slide 30: Basic Subnetting (3 subnets)
How about a local network that requires 3 subnets, given an address block 172.16.0.0 /16?
To provide 3 subnets, we need to create 4 subnets
  # of subnets = 2n
We borrow 2 bits to get a new prefix of /18 (or a subnet mask of 255.255.192.0)
How many usable addresses are there in each subnet?
  14 host bits
  # of usable addresses = 2h – 2 = 214 – 2 = 16382
Thus, the subnet 0 address would be 172.16.0.0/18
Notes: To provide 3 subnets, create 4 subnets
Borrow 2 bits, new prefix /18, subnet mask 255.255.192.0
Usable addresses per subnet is 2^14 -2 = 16382

## Slide 31: Basic Subnetting (3 subnets)
Starting with Subnet 0, derive the usable IP address range and broadcast address
Subnet 1 continues from where Subnet 0 end off
  Subnet 0 end off at the broadcast address 172.16.63.255
  Subnet 1 begins at the subnet 1 address 172.16.64.0 /18
Repeat for Subnet 2 and 3
Subnet | Subnet addr | Usable addr range | Broadcast addr
0 | 172.16.0.0 /18 | 172.16.0.1 – 172.16.63.254 | 172.16.63.255
1 | 172.16.64.0 /18 |  | 
2 |  |  | 
3 |  |  | 
172.16.64.1 – 172.16.127.254 172.16.127.255
172.16.128.0 /18 172.16.128.1 – 172.16.191.254 172.16.191.255
172.16.192.0 /18 172.16.192.1 – 172.16.255.254 172.16.255.255
Notes: To provide 3 subnets, create 4 subnets
Borrow 2 bits, new prefix /18, subnet mask 255.255.192.0
Usable addresses per subnet is 2^14 -2 = 16382

## Slide 32: Today’s Practical
Lab 1a: IPv4 Address Subnetting Part 1
  Determining network information
Lab 1b: Subnet and Router Configuration
  FLSM

## Slide 33: This Week’s Task
Revise CCNA 1: Network Fundamentals
  Chapter 6: Addressing the Network IPv4

## Slide 34: What’s On Next Week
Revision on IPv4 Address – VLSM
  Practical: Lab 1c (with VLSM rather than FLSM)
CCNA 3: LAN Switching and Wireless
Lecture:-
  Chapter 2: Basic Switch Concepts & Configuration
Tasks:-
  Read CCNA 3: Chapter 2 Basic Switch Concepts & Configuration

## Slide 35: Subnetting
VLSM subnetting

## Slide 36: Subnetting – VLSM
In traditional FLSM subnetting, the size of all the fixed blocks of subnets are determined by:-
  the largest subnet needed
  the number of subnets needed
If any of the subnets require only a few addresses, the rest of the addresses in that subnet are wasted
Variable Length Subnet Mask (VLSM) was designed to maximize addressing efficiency
Using VLSM addressing, always begin with the largest requirement to the smallest requirements (the WAN links)
Notes: And VLSM is easier to calculate compared to FLSM

## Slide 37: Subnetting – VLSM
You have been allocated the network address 192.168.15.0 /24. Given these network requirements, use VLSM to allocate subnets for these networks:-
  AtlantaHQ (58 hosts)
  SydneyHQ (10 hosts)
  PerthHQ (26 hosts)
  CorpusHQ (10 hosts)
  WAN link 1 (2 hosts)
  WAN link 2 (2 hosts)
  WAN link 3 (2 hosts)

## Slide 38: Subnetting – VLSM
Step 1: Set up a table with the subnet name or number, subnet address /prefix, usable address range and the broadcast address fields
Step 2: List the subnets in the order from the largest to the smallest hosts requirements:-
Subnet | Subnet Addr/Prefix | Usable Addr Range | Broadcast Addr
AtlantaHQ – 58 |  |  | 
PerthHQ – 26 |  |  | 
SydneyHQ – 10 |  |  | 
CorpusHQ – 10 |  |  | 
WAN1 – 2 |  |  | 
WAN2 – 2 |  |  | 
WAN3 – 2 |  |  | 

## Slide 39: Subnetting – VLSM
Begin with the 1st subnet:-
  How many minimum # of host bits needed to meet requirement?
  2h -2 ≥ host requirements
  h = 6 because 26 - 2 = 62, which is ≥ requirements of 58
  What is the new prefix? /26 because there are only 6 host bits
  What is the subnet address for the subnet 0?
  from the starting address block 192.168.15.0,
  adding the new prefix becomes 192.168.15.0 /26
  Calculate the usable addresses and broadcast address
Subnet | Subnet Addr/Prefix | Usable Addr Range | Broadcast Addr
AtlantaHQ – 58 | 192.168.15.0 /26 |  | 
192.168.15.1 – 192.168.15.63
192.168.15.62

## Slide 40: Subnetting – VLSM
The broadcast address of the last block is 192.168.15.63 /26
Thus the next address block to use is 192.168.15.64 /26
Approach the 2nd subnet (PerthHQ – 26):-
  How many minimum host bits needed to meet requirement? 5
  What is the new prefix? /27, (because there are 5 host bits)
  What is the subnet address? 192.168.15.64 /27
  Calculate the usable addresses and broadcast address
Subnet | Subnet Addr/Prefix | Usable Addr Range | Broadcast Addr
AtlantaHQ – 58 | 192.168.15.0 /26 | 192.168.15.1 – 192.168.15.62 | 192.168.15.63
PerthHQ – 26 | 192.168.15.64 /27 |  | 
192.168.15.65 – 192.168.15.95
192.168.15.94

## Slide 41: Subnetting – VLSM
Approach the 3rd subnet (SydneyHQ – 10):-
  How many minimum # of host bits needed to meet requirement? 4
  What is the new prefix? /28
  What is the subnet address? 192.168.15.96
  Calculate the usable addresses and broadcast address
Do the same for the 4th subnet (CorpusHQ – 10)
Subnet | Subnet Addr/Prefix | Usable Addr Range | Broadcast Addr
AtlantaHQ – 58 | 192.168.15.0 / 26 | 192.168.15.1 – 192.168.15.62 | 192.168.15.63
PerthHQ – 26 | 192.168.15.64 /27 | 192.168.15.65 – 192.168.15.94 | 192.168.15.95
SydneyHQ – 10 |  |  | 
192.168.15.96 /28 192.168.15.97 – 192.168.15.110 192.168.15.111
Notes: Next address block is 192.168.15.95 /27
Min # of host bits: 4
New prefix: /28
New subnet address: 192.168.15.96/28

## Slide 42: Subnetting – VLSM
Each WAN link subnet must be treated individually.
Approach the 5th subnet (WAN1– 2):-
  How many minimum # host bits needed to meet requirement? 2
  What is the prefix? /30
  What is the subnet address? 192.168.15.128
  Calculate the usable addresses and broadcast address
Do the same for the 6th and 7th WAN links subnets.
Subnet | Subnet Addr/Prefix | Usable Addr Range | Broadcast Addr
CorpusHQ – 10 | 192.168.15.112/28 | 192.168.15.113 – 192.168.15.126 | 192.168.15.127
WAN1 – 2 |  |  | 
192.168.15.128 /30 192.168.15.129 – 192.168.15.130 192.168.15.131
Notes: The next block address for the WAN is 192.168.15.128 /28
Host bits required = 2
Subnet prefix = /30
Subnet address = 192.168.15.128 /30

## Slide 43: Subnetting – VLSM
The entire table is:-
Subnet | Subnet Addr/Prefix | Usable Addr Range | Broadcast Addr
AtlantaHQ – 58 | 192.168.15.0 /26 | 192.168.15.1 – 192.168.15.62 | 192.168.15.63
PerthHQ – 26 | 192.168.15.64 /27 | 192.168.15.65 – 192.168.15.94 | 192.168.15.95
SydneyHQ – 10 | 192.168.15.96 /28 | 192.168.15.97 – 192.168.15.110 | 192.168.15.111
CorpusHQ – 10 | 192.168.15.112 /28 | 192.168.15.113 – 192.168.15.126 | 192.168.15.127
WAN1 – 2 | 192.168.15.128 /30 | 192.168.15.129 – 192.168.15.130 | 192.168.15.131
WAN2 – 2 | 192.168.15.132 /30 | 192.168.15.133 – 192.168.15.134 | 192.168.15.135
WAN3 – 2 | 192.168.15.136 /30 | 192.168.15.137 – 192.168.15.138 | 192.168.15.139

## Slide 44: Practise, Practise and Practise
Host addressing practice exercises at
  6.5.4 Determining the Network Address
  6.5.5 Calculating the Number of Hosts
  6.5.6 Determining Valid Addresses for Hosts

## Slide 45: Summary
Anatomy of an IPv4 address
Binary to Decimal; Decimal to Binary Conversion
3 Types of IPv4 addresses
  Network, usable hosts and Broadcast
Calculate Network, Host and Broadcast addresses
Subnetting with FLSM
Subnetting with VLSM

## Slide 46: Today’s Practical
Lab 1c: Subnet and Router Configuration
  VLSM