## Slide 1: Intrusion Detection and Prevention Systems
Chapter 11

## Slide 2: Intrusion Detection System
An IDS monitors traffic offline and generates an alert (log) when it detects malicious traffic including:
  Reconnaissance attacks
  Access attacks
  Denial of Service attacks
It is a passive device because it analyzes copies of the traffic stream traffic.
  Only requires a promiscuous interface.
  Does not slow network traffic.
  Allows some malicious traffic into the network.
Notes: The intrusion detection system (IDS) is a software- or hardware-based solution that passively listens to network traffic. The IDS is not in the traffic path, but listens promiscuously to all traffic on the network. Typically, only one promiscuous interface is required for network monitoring. Additional promiscuous interfaces can be used to monitor multiple networks. When the IDS detects malicious traffic, the IDS sends an alert to the management station.
The IDS has limited active response capabilities. When configured, the IDS can block further malicious traffic by actively configuring network devices (for example, security appliances or routers) in response to malicious traffic detection. However, the original malicious traffic has already passed through the network to the intended destination and cannot be blocked. Only subsequent traffic will be blocked. The IDS also has the capability of sending a TCP reset to the end host to terminate any malicious TCP connections.

## Slide 3: Intrusion Prevention System
It builds upon IDS technology to detect attacks.
  However, it can also immediately address the threat.
An IPS is an active device because all traffic must pass through it.
  Referred to as “inline-mode”, it works inline in real time to monitor Layer 2 through Layer 7 traffic and content.
  It can also stop single-packet attacks from reaching the target system (IDS cannot).

## Slide 4: Comparing IDS and IPS Solutions
 | IDS (Promiscuous Mode) | IPS (Inline Mode)
Advantages | No impact on network (latency, jitter). No network impact if there is a sensor failure or a sensor overload. | Stops trigger packets. Can use stream normalization techniques.
Disadvantages | Response action cannot stop trigger packets. Correct tuning required for response actions. More vulnerable to network evasion techniques. | Some impact on network (latency, jitter). Sensor failure or overloading impacts the network.

## Slide 5: IPS Signatures
To stop incoming malicious traffic, the network must first be able to identify it.
  Fortunately, malicious traffic displays distinct characteristics or "signatures."
A signature is a set of rules that an IDS and an IPS use to detect typical intrusive activity, such as DoS attacks.
  Signatures uniquely identify specific worms, viruses, protocol anomalies, or malicious traffic.
  IPS sensors are tuned to look for matching signatures or abnormal traffic patterns.
IPS signatures are conceptually similar to the virus.dat file used by virus scanners.

## Slide 6: Signature Attributes
Signatures have three distinctive attributes:
  Signature Type
    Atomic (one packet required)
    Composite (many packets required)
  Trigger (alarm)
  Action

## Slide 7: Signature Type – Atomic Signature
Simplest form of an attack as it consists of a single packet, activity, or event that is examined to determine if it matches a configured signature.
  If it does, an alarm is triggered, and a signature action is performed.
  It does not require any knowledge of past or future activities (No state information is required).

## Slide 8: Signature Type – Composite Signature
Also called a stateful signature, it identifies a sequence of operations distributed across multiple hosts over an arbitrary period of time (event horizon).
  Event horizon: The length of time that the signatures must maintain state.
Usually requires several pieces of data to match an attack signature, and an IPS device must maintain state.

## Slide 9: Signature Type – Composite Signature
The length of an event horizon varies from one signature to another.
  An IPS cannot maintain state information indefinitely without eventually running out of resources.
Therefore, an IPS uses a configured event horizon to determine how long it looks for a specific attack signature when an initial signature component is detected.
  Configuring the length of the event horizon is a tradeoff between consuming system resources and being able to detect an attack that occurs over an extended period of time.

## Slide 10: Signature File
As new threats are identified, new signatures must be created and uploaded to an IPS.
To make this process easier, all signatures are contained in a signature file and uploaded to an IPS on a regular basis.
  Networks deploying the latest signature files are better protected against network intrusions.

## Slide 11: Updating Signatures
Cisco investigates / creates signatures for new threats as they are discovered and publishes them regularly.
  Lower priority IPS signature files are published biweekly.
  If the threat is severe, Cisco publishes signature files within hours of identification.
Update the signature file regularly to protect the network.
  Each update includes new signatures and all the signatures in the previous version.
    For example, signature file IOS-S361-CLI.pkg includes all signatures in file IOS-S360-CLI.pkg plus signatures created for threats discovered subsequently.
New signatures are downloadable from CCO.
  Requires a valid CCO login.

## Slide 12: Updating Signatures

## Slide 13: Signature Trigger (Signature Alarm)
The signature trigger for an IPS sensor is anything that can reliably signal an intrusion or security policy violation.
  E.g., a packet with a payload containing a specific string going to a specific port.
Four types of signature triggers:
  Pattern-based detection
  Policy-based detection
  Anomaly-based detection
  Reputation-based detection

## Slide 14: Pattern-Based Detection
Pattern-based detection (signature-based detection), is the simplest triggering mechanism because it searches for a specific, pre-defined pattern.
The IPS sensor compares the network traffic to a database of known attacks and triggers an alarm or prevents communication if a match is found.

## Slide 15: Policy-Based Detection
Similar to pattern-based detection, but instead of trying to define specific patterns, the administrator defines behaviors that are suspicious based on historical analysis.

## Slide 16: Anomaly-Based Detection
It can detect new and previously unpublished attacks.
Normal activity is defined and any activity that deviates from this profile is abnormal and triggers a signature action.
  Note that an alert does not necessarily indicate an attack since a small deviation can sometimes occur from valid user traffic.
  As the network evolves, the definition of normal usually changes, so the definition of normal must be redefined.

## Slide 17: Reputation- Based Detection
Ability to track the reputation of specific addresses and domains on the Internet.
Reputation scores decrease if domain is showing signs of malicious activity (e.g. Domain is more than 24hrs old and has sourced 10M emails in 24 hrs and IP is changing)
Reputation scores provide the IPS device a measure when deciding whether to drop or permit traffic.
Reputation tracking can change and is very dynamic

## Slide 18: Tuning Alarms
Triggering mechanisms can generate various types of alarms including:
Tune alarm
Alarm generated
Normal user traffic
False positive
Tune alarm
No alarm generated
Attack traffic
False negative
Ideal setting
Ideal setting
Outcome
True negative
True positive
Alarm Type
No alarm generated
Normal user traffic
Alarm generated
Attack traffic
IPS Activity
Network Activity

## Slide 19: Tuning Alarms
False Positive:
  False positive alarm is an expected but undesired result.
  It occurs when an intrusion system generates an alarm after processing normal user traffic that should not have resulted in the alarm.
  The administrator must be sure to tune the IPS to change these alarm types to true negatives.
False Negative:
  The IPS fails to generate an alarm after processing attack traffic that it is configured to detect.
  It is imperative that the IPS does not generate false negatives, because it means that known attacks are not being detected.
  The goal is to render these alarm types as true positive.

## Slide 20: Types of Signature Triggers
 | Advantages | Disadvantages
Pattern detection (Signature-based) | Easy configuration Fewer false positives Good signature design | No detection of unknown signatures Initially a lot of false positives Signatures must be created, updated, and tuned
Policy-based detection (Behavior-based) | Simple and reliable Customized policies Can detect unknown attacks | Generic output Policy must be created
Anomaly detection (Profile-based) | Easy configuration Can detect unknown attacks | Difficult to profile typical activity in large networks Traffic profile must be constant
Reputation Based detection | can determine dynamically the reputation of source Can detect unknown attacks | Difficult to profile typical activity Policy must be created

## Slide 21: IPS Signature Actions
Whenever a signature detects the activity for which it is configured, the signature triggers one or more actions.
Several actions can be performed:
  Allow the activity.
  Drop or prevent the activity.
  Block future activity.
  Generate an alert.
  Log the activity.
  Reset a TCP connection.

## Slide 22: IPS Signature Actions
Category | Specific Alert | Description
Generating an alert | Produce alert | This action writes the event to the Event Store as an alert.
 | Produce verbose alert | This action includes an encoded dump of the offending packet in the alert.
Logging the activity | Log attacker packets | This action starts IP logging on packets that contain the attacker address and sends an alert.
 | Log pair packets | This action starts IP logging on packets that contain the attacker and victim address pair.
 | Log victim packets | This action starts IP logging on packets that contain the victim address and sends an alert.
Dropping or preventing the activity | Deny attacker inline | This action terminates the current packet and future packets from this attacker address for a specified period of time. The sensor maintains a list of the attackers currently being denied by the system. Entries may be removed from the list manually or wait for the timer to expire. The timer is a sliding timer for each entry. Therefore, if attacker A is currently being denied, but issues another attack, the timer for attacker A is reset and attacker A remains on the denied attacker list until the timer expires. If the denied attacker list is at capacity and cannot add a new entry, the packet is still denied.
 | Deny connection inline | This action terminates the current packet and future packets on this TCP flow.
 | Deny packet inline | This action terminates the packet.

## Slide 23: IPS Signature Actions
Category | Specific Alert | Description
Resetting a TCP connection | Reset TCP connection | This action sends TCP resets to hijack and terminate the TCP flow.
Blocking future activity | Request block connection | This action sends a request to a blocking device to block this connection.
 | Request block host | This action sends a request to a blocking device to block this attacker host.
 | Request SNMP trap | This action sends a request to the notification application component of the sensor to perform Simple Network Management Protocol (SNMP) notification.
Please watch video on IPS:
https://www.youtube.com/watch?v=BKhCR7tNUss

## Slide 24: Implementing IPS

## Slide 25: Steps to implement Cisco IOS IPS
Download the IOS IPS files.
Create an IOS IPS configuration directory in flash.
Configure an IOS IPS crypto key.
Enable IOS IPS (consists of several substeps).
Load the IOS IPS signature package to the router.

## Slide 26: 1. Download the IOS IPS files.
Download the IOS IPS signature file and public crypto key from cisco.com.
  IOS-Sxxx-CLI.pkg - Format of the latest signature package.
  realm-cisco.pub.key.txt - Public crypto key used by IOS IPS.
The specific IPS files to download vary depending on the current release.
  Only registered customers can download the package files and key.
Notes: Cisco SDFs are updated and posted to Cisco.com on a regular basis. Thus, customers can download signatures that help protect networks from the latest known network attacks.
Multiple definition sources are available, such as the default, built-in signatures that are shipped with the routers, or the SDF files named 64MB.sdf, 128MB.sdf, and 256MB.sdf. The files differ in the number of configured signatures. The administrator should select the appropriate SDF file based on the amount of RAM memory in the router.

## Slide 27: 2. Create an IOS IPS directory in Flash
Create a directory in flash to store the signature files and configurations.
  Use the mkdir directory-name privileged EXEC command to create the directory.
  Use the rename current-name new-name command to change the name of the directory.
To verify the contents of flash, enter the dir flash: privileged EXEC command.
R1# mkdir ips
Create directory filename [ips]?
Created dir flash:ips
R1#
R1# dir flash:
Directory of flash:/
5 -rw- 51054864 Jan 10 2009 15:46:14 -08:00
c2800nm-advipservicesk9-mz.124-20.T1.bin
6 drw- 0 Jan 15 2009 11:36:36 -08:00 ips
64016384 bytes total (12693504 bytes free)
R1#

## Slide 28: 3. Configure an IOS IPS crypto key
Step 1: Open the text file, realm-cisco.pub.key.txt ,copy the contents of the file
Step 2: Use the “configure terminal” command to enter config mode
Step 3: Paste the text it in the global configuration prompt after the #
  The text file issues the various commands to generate the RSA key.
Step 4: You can #show run to verify that the crypto key is configured.
The crypto key is used to verify the digital signature for the master signature file (sigdef-default.xml) whose contents are signed by a Cisco private key to guarantee its authenticity and integrity at every release.

## Slide 29: 3. Configure an IOS IPS crypto key
Highlight and copy the text in the public key file.
Paste the copied text at the global config prompt.
R1# conf t
R1(config)#

## Slide 30: 3. Configure an IOS IPS crypto key
Issue the show run command to verify that the key was copied.
R1# show run
<Output omitted>
crypto key pubkey-chain rsa
named-key realm-cisco.pub signature
key-string
30820122 300D0609 2A864886 F70D0101 01050003 82010F00 3082010A 02820101
00C19E93 A8AF124A D6CC7A24 5097A975 206BE3A2 06FBA13F 6F12CB5B 4E441F16
17E630D5 C02AC252 912BE27F 37FDD9C8 11FC7AF7 DCDD81D9 43CDABC3 6007D128
B199ABCB D34ED0F9 085FADC1 359C189E F30AF10A C0EFB624 7E0764BF 3E53053E
5B2146A9 D7A5EDE3 0298AF03 DED7A5B8 9479039D 20F30663 9AC64B93 C0112A35
FE3F0C87 89BCB7BB 994AE74C FA9E481D F65875D6 85EAF974 6D9CC8E3 F0B08B85
50437722 FFBE85B9 5E4189FF CC189CB9 69C46F9C A84DFBA5 7A0AF99E AD768C36
006CF498 079F88F8 A3B3FB1F 9FB7B3CB 5539E1D1 9693CCBB 551F78D2 892356AE
2F56D826 8918EF3C 80CA4F4D 87BFCA3B BFF668E9 689782A5 CF31CB6E B4B094D3
F3020301 0001
<Output omitted>

## Slide 31: 3. Configure an IOS IPS crypto key
At the time of signature compilation, an error message is generated if the public crypto key is invalid.
  If the key is configured incorrectly, the key must be removed and then reconfigured using the no crypto key pubkey-chain rsa and the no named-key realm-cisco.pub signature commands.

## Slide 32: 4a. Enable IOS IPS
Identify the IPS rule name and specify the location.
  Use the ip ips name [rule name] [optional ACL] command to create a rule name.
  You can specify an optional extended or standard access control list (ACL) in order to filter the traffic that will be scanned by this rule name. All traffic that is permitted by the ACL is subject to inspection by the IPS. Traffic that is denied by the ACL is not inspected by the IPS.
Use the ip ips config location flash:directory-name command to configure the IPS signature storage location.
R1(config)# ip ips name IOSIPS
R1(config)# ip ips name ips list ?
<1-199> Numbered access list
WORD Named access list
R1(config)#
R1(config)# ip ips config location flash:ips
R1(config)#

## Slide 33: 4b. Enable IOS IPS
Enable SDEE and HTTP.
  Security Device Event Exchange (SDEE) is an application-level communication protocol that is used to exchange IPS messages between IPS clients and IPS servers.
  SDEE is always running, but it does not receive and process events from IPS unless SDEE notification is enabled. If SDEE notification is not enabled and a client sends a request, SDEE responds with a fault response message, indicating that notification is not enabled
  SDEE notification must be explicitly enabled using the ip ips notify sdee command.
  The HTTP server must first be enabled using the ip http server command. If the HTTP server is not enabled, the router cannot respond to the SDEE clients because it cannot see the requests.

## Slide 34: 4b. Enable IOS IPS
IOS IPS also supports logging to send event notification.
  SDEE and logging can be used independently or simultaneously.
  Logging notification is enabled by default.
  Use the ip ips notify log command to enable logging.
R1(config)# ip http server
R1(config)# ip ips notify sdee
R1(config)# ip ips notify log
R1(config)#

## Slide 35: 4c. Configure the Signature Category
All signatures are grouped into three common categories:
  All
  Basic
  Advanced
Signature Categories and Signatures that IOS IPS uses to scan traffic can be retired or unretired.
  Retired means that IOS IPS does not compile that signature into memory.
  Unretired instructs the IOS IPS to compile the signature into memory and use it to scan traffic.

## Slide 36: 4c. Configure the Signature Category
When IOS IPS is first configured, all signatures in the all category should be retired, and then selected signatures should be unretired in a less memory-intensive category.
  To retire and unretired signatures, first enter IPS category mode using the ip ips signature-category command.
  Next use the category category-name command to change a category.
R1(config)# ip ips signature-category
R1(config-ips-category)# category all
R1(config-ips-category-action)# retired true
R1(config-ips-category-action)# exit
R1(config-ips-category)#
R1(config-ips-category)# category IOSIPS basic
R1(config-ips-category-action)# retired false
R1(config-ips-category-action)# exit
R1(config-ips-category)# exit
Do you want to accept these changes? [confirm] y
R1(config)#

## Slide 37: 4d. Configure the Signature Category
Apply the IPS rule to a desired interface, and specify the direction.
Use the ip ips rule-name [in | out] interface configuration command to apply the IPS rule.
  The in argument means that only traffic going into the interface is inspected by IPS.
  The out argument specifies that only traffic going out of the interface is inspected.
R1(config)# interface GigabitEthernet 0/1
R1(config-if)# ip ips IOSIPS in
R1(config-if)# ip ips IOSIPS out
R1(config-if)# exit
R1(config)# exit

## Slide 38: 5. Load the IOS IPS signature
Load the signature package (IOS-Sxxx-CLI.pkg) to the router using either FTP or TFTP.
  To copy the downloaded signature package from the FTP server to the router, make sure to use the idconf parameter at the end of the command.
  copy ftp://ftp_user:password@Server_IP_address/signature_package idconf
R1# copy ftp://cisco:cisco@10.1.1.1/IOS-S376-CLI.pkg idconf
Loading IOS-S310-CLI.pkg !!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
[OK - 7608873/4096 bytes]
*Jan 15 16:44:47 PST: %IPS-6-ENGINE_BUILDS_STARTED: 16:44:47 PST Jan 15 2008
*Jan 15 16:44:47 PST: %IPS-6-ENGINE_BUILDING: multi-string - 8 signatures - 1 of 13 engines
*Jan 15 16:44:47 PST: %IPS-6-ENGINE_READY: multi-string - build time 4 ms - packets for this engine will be scanned
*Jan 15 16:44:47 PST: %IPS-6-ENGINE_BUILDING: service-http - 622 signatures - 2 of 13 engines
*Jan 15 16:44:53 PST: %IPS-6-ENGINE_READY: service-http - build time 6024 ms - packets for this engine will be scanned
<Output omitted>

## Slide 39: 5. Load the IOS IPS signature
Verify that the signature package is properly compiled using the show ip ips signature count command.
R1# show ip ips signature count
Cisco SDF release version S310.0 ← signature package release version
Trend SDF release version V0.0
Signature Micro-Engine: multi-string: Total Signatures 8
multi-string enabled signatures: 8
multi-string retired signatures: 8
<output omitted>
Signature Micro-Engine: service-msrpc: Total Signatures 25
service-msrpc enabled signatures: 25
service-msrpc retired signatures: 18
service-msrpc compiled signatures: 1
service-msrpc inactive signatures - invalid params: 6
Total Signatures: 2136
Total Enabled Signatures: 807
Total Retired Signatures: 1779
Total Compiled Signatures:
351 ← total compiled signatures for the IOS IPS Basic category
Total Signatures with invalid parameters: 6
Total Obsoleted Signatures: 11
R1#

## Slide 40: Modifying Signatures
This example shows how to retire individual signatures.
  In this example, signature 6130 with subsig ID of 10 is retired.
R1# configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# ip ips signature-definition
R1(config-sigdef)# signature 6130 10
R1(config-sigdef-sig)# status
R1(config-sigdef-sig-status)# retired true
R1(config-sigdef-sig-status)# exit
R1(config-sigdef-sig)# exit
R1(config-sigdef)# exit
Do you want to accept these changes? [confirm] y
R1(config)#

## Slide 41: Modifying Signatures
This example shows how to unretire all signatures that belong to the IOS IPS Basic category. (Prev example)
R1# configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# ip ips signature-category
R1(config-ips-category)# category ios_ips basic
R1(config-ips-category-action)# retired false
R1(config-ips-category-action)# exit
R1(config-ips-category)# exit
Do you want to accept these changes? [confirm] y
R1(config)#

## Slide 42: Change Actions for a Signature
This example shows how to change signature actions to alert, drop, and reset for signature 6130 with subsig ID of 10.
R1# configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# ip ips signature-definition
R1(config-sigdef)# signature 6130 10
R1(config-sigdef-sig)# engine
R1(config-sigdef-sig-engine)# event-action produce-alert
R1(config-sigdef-sig-engine)# event-action deny-packet-inline
R1(config-sigdef-sig-engine)# event-action reset-tcp-connection
R1(config-sigdef-sig-engine)# exit
R1(config-sigdef-sig)# exit
R1(config-sigdef)# exit
Do you want to accept these changes? [confirm] y
R1(config)

## Slide 43: Change Actions for a Category
This example shows how to change event actions for all signatures that belong to the signature IOS IPS Basic category.
R1# configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# ip ips signature-category
R1(config-ips-category)# category ios_ips basic
R1(config-ips-category-action)# event-action produce-alert
R1(config-ips-category-action)# event-action deny-packet-inline
R1(config-ips-category-action)# event-action reset-tcp-connection
R1(config-ips-category-action)# exit
R1(config-ips-category)# exit
Do you want to accept these changes? [confirm] y
R1(config)#

## Slide 44: Verify IOS IPS
R1# show ip ips all
IPS Signature File Configuration Status Configured Config Locations: flash:/ipsdir/ Last signature default load time: 04:39:33 UTC Jan 15 2009 Last signature delta load time: -none- Last event action (SEAP) load time: -none-
General SEAP Config: Global Deny Timeout: 3600 seconds Global Overrides Status: Enabled Global Filters Status: Enabled
IPS Auto Update is not currently configured
IPS Syslog and SDEE Notification Status
Event notification through syslog is enabled
Event notification through SDEE is enabled
IPS Signature Status
Total Active Signatures: 693
Total Inactive Signatures: 1443
IPS Packet Scanning and Interface Status
IPS Rule Configuration
IPS name myips
IPS fail closed is disabled
IPS deny-action ips-interface is false
Fastpath ips is enabled
Quick run mode is enabled
Interface Configuration
Interface FastEthernet0/1
Inbound IPS rule is not set
Outgoing IPS rule is myips
<output omitted>

## Slide 45: View Configuration
R1# show ip ips configuration
Event notification through syslog is enabled
Event notification through Net Director is enabled
Default action(s) for info signatures is alarm
Default action(s) for attack signatures is alarm
Default threshold of recipients for spam signature is 25
PostOffice:HostID:5 OrgID:100 Addr:10.2.7.3 Msg dropped:0
HID:1000 OID:100 S:218 A:3 H:14092 HA:7118 DA:0 R:0
CID:1 IP:172.21.160.20 P:45000 S:ESTAB (Curr Conn)
Audit Rule Configuration
Audit name AUDIT.1
info actions alarm
<output omitted>

## Slide 46: View IPS Interface Configuration
R1# show ip ips interfaces
Interface Configuration
Interface FastEthernet0/0
Inbound IPS rule is sdm_ips_rule
Outgoing IPS rule is not set
Interface FastEthernet0/1
Inbound IPS rule is sdm_ips_rule
Outgoing IPS rule is not set
R1#

## Slide 47: Show Signature Status
R1# show ip ips signature | include 5000
SigID:SubID On Action Sev Trait MH AI CT TI AT FA WF Version
----------- -- ------ --- ----- -- -- -- -- ----- ----------
50000:0 N A HIGH 0 0 0 0 0 FA N OPACL
50000:1 N A HIGH 0 0 0 0 0 FA N OPACL
50000:2 N A HIGH 0 0 0 0 0 FA N OPACL
R1#

## Slide 48: View Alarm and Packet Statistics
R1# show ip ips statistics
Signature audit statistics [process switch:fast switch]
signature 2000 packets audited: [0:2]
signature 2001 packets audited: [9:9]
signature 2004 packets audited: [0:2]
signature 3151 packets audited: [0:12]
Interfaces configured for audit 2
Session creations since subsystem startup or last reset 11
Current session counts (estab/half-open/terminating) [0:0:0]
Maxever session counts (estab/half-open/terminating) [2:1:0]
Last session created 19:18:27
Last statistic reset never
HID:1000 OID:100 S:218 A:3 H:14085 HA:7114 DA:0 R:0
R1#

## Slide 49
Difference between Firewalls and IPS
https://ipwithease.com/firewall-vs-ips-vs-ids/

## Slide 50
Parameters | Firewall (SPI) | IPS | IDS
Definition | Firewall is a network security device that filters incoming and outgoing traffic based on predefined rules | IPS is a device that inspects traffic, detects anomalies and proactively stops malicious traffics based on updated signatures | IDS is a device that monitors traffic for anomalies and send an alert upon detection based on updated signatures
Detects threats based on : | IP addresses and port numbers (generally Stateful Packet Inspection) and blocks traffic | Traffic patterns and signatures of attack and prevents them | Traffic patterns and signatures of attack and alerts only
Layers | Layer 3 mode | Layers 2 and above | Layers 2 and above
Placement | 1st line of defence | Placed after a firewall, “inline” to traffic | Placed after a firewall, not “inline” to traffic
 | Protocol /port rules based Blocks attacks | Anomaly Based detection Signature detection Zero day attacks Blocks attacks | Anomaly Based detection Signature detection Zero day attacks Send Alarms
Difference between Firewalls and IPS

## Slide 51: The End