## Slide 1: Chapter 3a: VLANs
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 2: Overview of VLANs Types of VLANs (cont.)
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.3 – Types of VLANs (cont.)

## Slide 3: VLANs in a Multi-Switched Environment VLAN Trunks
The links between switches S1 and S2, and S1 and S3 are configured to transmit traffic coming from VLANs 10, 20, 30, and 99 across the network. This network could not function without VLAN trunks.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.1 – VLAN Trunks

## Slide 4: VLANs in a Multi-Switched Environment VLAN Trunks (cont.)
A VLAN trunk is a point-to-point link that carries more than one VLAN.
A VLAN trunk is usually established between switches so same-VLAN devices can communicate, even if physically connected to different switches.
A VLAN trunk is not associated to any VLANs; neither is the trunk ports used to establish the trunk link.
Cisco IOS supports IEEE802.1q, a popular VLAN trunk protocol.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.1 – VLAN Trunks (cont.)

## Slide 5: VLAN Assignment VLAN Ranges on Catalyst Switches (cont.)
Normal Range VLANs
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.1 - VLAN Ranges on Catalyst Switches

## Slide 6: VLAN Assignment Creating a VLAN
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.2 – Creating a VLAN

## Slide 7: VLAN Assignment Assigning Ports to VLANs
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.3 – Assigning Ports to VLANs

## Slide 8: VLAN Assignment Changing VLAN Port Membership
Remove VLAN Assignment
Interface F0/18 was previously assigned to VLAN 20 which is still active, F0/18 reset to VLAN1
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.4 - Changing VLAN Port Membership

## Slide 9: VLAN Assignment Changing VLAN Port Membership (cont.)
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.4 - Changing VLAN Port Membership (cont.)

## Slide 10: VLAN Assignment Changing VLAN Port Membership (cont.)
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.4 - Changing VLAN Port Membership (cont.)

## Slide 11: VLAN Assignment Deleting VLANs
The entire vlan.dat file can be deleted using the delete flash:vlan.dat privileged EXEC mode command
Abbreviated command version (delete vlan.dat) can be used if the vlan.dat file has not been moved from its default location
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.5 – Deleting VLANs

## Slide 12: VLAN Assignment Verifying VLAN Information
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.6 - Verifying VLAN Information

## Slide 13: VLAN Assignment Verifying VLAN Information (cont.)
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.6 - Verifying VLAN Information

## Slide 14: VLAN Trunks Configuring IEEE 802.1q Trunk Links
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.1 - Configuring IEEE 802.1q Trunk Links

## Slide 15: VLAN Assignment Configuring IEEE 802.1q Trunk Links (cont.)
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.1 - Configuring IEEE 802.1q Trunk Links (cont.)

## Slide 16: VLAN Trunks Resetting the Trunk to Default State
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.2 - Resetting the Trunk to Default State

## Slide 17: VLAN Trunks Resetting the Trunk to Default State (cont.)
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.2 - Resetting the Trunk to Default State (cont.)

## Slide 18: VLAN Trunks Verifying Trunk Configuration
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunk
6.2.2.3 - Verifying Trunk Configuration

## Slide 19: Troubleshoot VLANs and Trunks IP Addressing Issues with VLANs
It is a common practice to associate a VLAN with an IP network.
Because different IP networks only communicate through a router, all devices within a VLAN must be part of the same IP network to communicate.
The figure displays that PC1 cannot communicate to the server because it has a wrong IP address configured.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.1 - IP Addressing Issues with VLANs

## Slide 20: Troubleshoot VLANs and Trunks Missing VLANs
If all the IP address mismatches have been solved, but the device still cannot connect, check if the VLAN exists in the switch.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.2 - Missing VLANs

## Slide 21: Troubleshoot VLANs and Trunks Missing VLANs (cont.)
If the VLAN to which a port belongs is deleted, the port becomes inactive. All ports belonging to the VLAN that was deleted are unable to communicate with the rest of the network.
Not functional until the missing VLAN is created using the vlan vlan_id global configuration.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.2 - Missing VLANs (cont.)

## Slide 22: Troubleshoot VLANs and Trunks Introduction to Troubleshooting Trunks
  Note: To solve a native VLAN mismatch, configure the native VLAN to be the same VLAN on both sides of the link.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.3 - Introduction to Troubleshooting Trunks

## Slide 23: Troubleshoot VLANs and Trunks Common Problems with Trunks
Trunking issues are usually associated with incorrect configurations.
The most common type of trunk configuration errors are:
    Native VLAN mismatches
    Trunk mode mismatches
    Allowed VLANs on trunks
If a trunk problem is detected, the best practice guidelines recommend to troubleshoot in the order shown above.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.4 - Common Problems with Trunks

## Slide 24: Troubleshoot VLANs and Trunks Common Problems with Trunks (cont.)
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.4 - Common Problems with Trunks

## Slide 25: Troubleshoot VLANs and Trunks Incorrect Port Mode
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.5 - Incorrect Port Mode

## Slide 26: Troubleshoot VLANs and Trunks Incorrect VLAN List
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.6 - Incorrect VLAN List

## Slide 27: Troubleshoot VLANs and Trunks Incorrect VLAN List (cont.)
VLANs must be allowed in the trunk before their frames can be transmitted across the link.
Use the switchport trunk allowed vlan command to specify which VLANs are allowed in a trunk link.
Use the show interfaces trunk command to ensure the correct VLANs are permitted in a trunk.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.6 - Incorrect VLAN List (cont.)

## Slide 28: Inter-VLAN Routing Operation Router-on-a-Stick Inter-VLAN Routing
The router-on-a-stick approach uses only one of the router’s physical interface.
One of the router’s physical interfaces is configured as a 802.1Q trunk port so it can understand VLAN tags.
Logical subinterfaces are created; one subinterface per VLAN.
Each subinterface is configured with an IP address from the VLAN it represents.
VLAN members (hosts) are configured to use the subinterface address as a default gateway.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.1 – Inter-VLAN Routing Operation
6.3.1.3 - Router-on-a-Stick Inter-VLAN Routing

## Slide 29: Inter-VLAN Routing Operation Router-on-a-Stick Inter-VLAN Routing (cont.)
Router interface configured to operate as a trunk link and is connected to a trunked switch port. The router performs inter-VLAN routing by accepting VLAN-tagged traffic on the trunk interface coming from the adjacent switch, and then, internally routing between the VLANs using subinterfaces. The router then forwards the routed traffic, VLAN-tagged for the destination VLAN, out the same physical interface as it used to receive the traffic.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.1 – Inter-VLAN Routing Operation
6.3.1.3 - Router-on-a-Stick Inter-VLAN Routing (cont.)

## Slide 30: Configure Legacy Inter-VLAN Routing Configure Legacy Inter-VLAN Routing: Switch Configuration
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.2 – Configure Legacy Inter-VLAN Routing
6.3.2.2 - Configure Legacy Inter-VLAN Routing: Switch Configuration

## Slide 31: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Preparation
An alternative to legacy inter-VLAN routing is to use VLAN trunking and subinterfaces.
VLAN trunking allows a single physical router interface to route traffic for multiple VLANs.
The physical interface of the router must be connected to a trunk link on the adjacent switch.
On the router, subinterfaces are created for each unique VLAN.
Each subinterface is assigned an IP address specific to its subnet or VLAN and is also configured to tag frames for that VLAN.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.1 - Configure Router-on-a Stick: Preparation

## Slide 32: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Switch Configuration
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.2 - Configure Router-on-a Stick: Switch Configuration

## Slide 33: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Router Subinterface Configuration
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.3 - Configure Router-on-a Stick: Router Subinterface Configuration

## Slide 34: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Verifying Subinterfaces
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.4 - Configure Router-on-a Stick: Verifying Subinterfaces

## Slide 35: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Verifying Subinterfaces (cont.)
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.2 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.4 - Configure Router-on-a Stick: Verifying Subinterfaces (cont.)

## Slide 36: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Verifying Routing
Access to devices on remote VLANs can be tested using the ping command.
The ping command sends an ICMP echo request to the destination address.
When a host receives an ICMP echo request, it responds with an ICMP echo reply.
Tracert is a useful utility for confirming the routed path taken between two devices.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.5 - Configure Router-on-a Stick: Verifying Routing