## Slide 1: Chapter 3b: Access Control Lists
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: Access Control Lists

## Slide 2: Purpose of ACLs What is an ACL?
By default, a router does not have ACLs configured; therefore, by default a router does not filter traffic.
Notes: 7.1 – ACL Operation
7.1.1 – Purpose of ACLs
7.1.1.1 – What is an ACL?

## Slide 3: Purpose of ACLs Packet Filtering
Packet filtering, sometimes called static packet filtering, controls access to a network by analyzing the incoming and outgoing packets and passing or dropping them based on given criteria, such as the source IP address, destination IP addresses, and the protocol carried within the packet.
A router acts as a packet filter when it forwards or denies packets according to filtering rules.
An ACL is a sequential list of permit or deny statements, known as access control entries (ACEs).
Notes: 7.1 – ACL Operation
7.1.1 – Purpose of ACLs
7.1.1.2 – Packet Filtering

## Slide 4: Purpose of ACLs ACL Operation
Notes: 7.1 – ACL Operation
7.1.1 – Purpose of ACLs
7.1.1.3 – ACL Operation

## Slide 5: Wildcard Masks in ACLs Introducing ACL Wildcard Masking
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.1 – Introducing ACL Wildcard Masking

## Slide 6: Wildcard Masks in ACLs Introducing ACL Wildcard Masking (cont.)
Example
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.1 – Introducing ACL Wildcard Masking (cont.)

## Slide 7: Wildcard Masks in ACLs Wildcard Mask Examples
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.2 - Wildcard Mask Examples

## Slide 8: Wildcard Masks in ACLs Wildcard Mask Examples (cont.)
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.2 - Wildcard Mask Examples

## Slide 9: Wildcard Masks in ACLs Calculating the Wildcard Mask
Calculating wildcard masks can be challenging. One shortcut method is to subtract the subnet mask from 255.255.255.255.
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.3 - Calculating the Wildcard Mask

## Slide 10: Wildcard Masks in ACLs Wildcard Mask Keywords
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.4 - Wildcard Mask Keywords

## Slide 11: Wildcard Masks in ACLs Wildcard Mask Keyword Examples
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.5 - Wildcard Mask Keyword Examples

## Slide 12: Guidelines for ACL Creation General Guidelines for Creating ACLS
Notes: 7.1 – ACL Operation
7.1.3 – Guidelines for ACL Creation
7.1.3.1 - General Guidelines for Creating ACLS

## Slide 13: Guidelines for ACL Creation ACL Best Practices
Notes: 7.1 – ACL Operation
7.1.3 – Guidelines for ACL Creation
7.1.3.2 - ACL Best Practices

## Slide 14: Guidelines for ACL Placement Where to Place ACLs
Notes: 7.1 – ACL Operation
7.1.4 – Guidelines for ACL Placement
7.1.4.1 - Where to Place ACLs

## Slide 15: Guidelines for ACL Placement Where to Place ACLs (cont.)
Every ACL should be placed where it has the greatest impact on efficiency. The basic rules are:
  Extended ACLs - Locate extended ACLs as close as possible to the source of the traffic to be filtered.
  Standard ACLs - Because standard ACLs do not specify destination addresses, place them as close to the destination as possible.
  Placement of the ACL, and therefore the type of ACL used, may also depend on: the extent of the network administrator’s control, bandwidth of the networks involved, and ease of configuration.
Notes: 7.1 – ACL Operation
7.1.4 – Guidelines for ACL Placement
7.1.4.1 - Where to Place ACLs

## Slide 16: Guidelines for ACL Placement Standard ACL Placement
The administrator wants to prevent traffic originating in the 192.168.10.0/24 network from reaching the 192.168.30.0/24 network.
Notes: 7.1 – ACL Operation
7.1.4 – Guidelines for ACL Placement
7.1.4.2 - Standard ACL Placement

## Slide 17: 7.2 Standard IPv4 ACLs
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: VLANs

## Slide 18: Configure Standard IPv4 ACLs Numbered Standard IPv4 ACL Syntax
Router(config)# access-list access-list-number { deny | permit | remark } source [ source-wildcard ] [ log ]
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.1 - Numbered Standard IPv4 ACL Syntax

## Slide 19: Configure Standard IPv4 ACLs Applying Standard IPv4 ACLs to Interfaces
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.2 - Applying Standard IPv4 ACLs to Interfaces

## Slide 20: Configure Standard IPv4 ACLs Applying Standard IPv4 ACLs to Interfaces (cont.)
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.2 - Applying Standard IPv4 ACLs to Interfaces

## Slide 21: Configure Standard IPv4 ACLs Numbered Standard IPv4 ACL Examples
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.3 - Numbered Standard IPv4 ACL Examples

## Slide 22: Configure Standard IPv4 ACLs Numbered Standard IPv4 ACL Examples (cont.)
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.3 - Numbered Standard IPv4 ACL Examples

## Slide 23: Configure Standard IPv4 ACLs Named Standard IPv4 ACL Syntax
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.4 - Named Standard IPv4 ACL Syntax

## Slide 24: Configure Standard IPv4 ACLs Named Standard IPv4 ACL Syntax (cont.)
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.4 - Named Standard IPv4 ACL Syntax

## Slide 25: Modify IPv4 ACLs Method 1 – Use a Text Editor
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.1 - Method 1 – Use a Text Editor

## Slide 26: Modify IPv4 ACLs Method 2 – Use Sequence Numbers
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.2 - Method 2 – Use Sequence Numbers

## Slide 27: Modify IPv4 ACLs Editing Standard Named ACLs
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.3 - Editing Standard Named ACLs

## Slide 28: Modify IPv4 ACLs Verifying ACLs
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.4 - Verifying ACLs

## Slide 29: Modify IPv4 ACLs ACL Statistics
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.5 - ACL Statistics

## Slide 30: Securing VTY Ports with a Standard IPv4 ACL The access-class Command
The access-class command configured in line configuration mode restricts incoming and outgoing connections between a particular VTY (into a Cisco device) and the addresses in an access list.
Notes: 7.2 – Standard IPv4 ACLs
7.2.3 – Securing VTY Ports with a Standard IPv4 ACL
7.2.3.1 - The access-class Command

## Slide 31: Securing VTY Ports with a Standard IPv4 ACL Verifying the VTY Port is Secured
Notes: 7.2 – Standard IPv4 ACLs
7.2.3 – Securing VTY Ports with a Standard IPv4 ACL
7.2.3.2 - Verifying the VTY Port is Secured

## Slide 32: 7.3 Troubleshoot ACLs
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: Access Control Lists

## Slide 33: Processing Packet with ACLs The Implicit Deny Any
At least one permit ACE must be configured in an ACL or all traffic is blocked.
For the network in the figure, applying either ACL 1 or ACL 2 to the S0/0/0 interface of R1 in the outbound direction will have the same effect.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.1 - The Implicit Deny Any

## Slide 34: Processing Packet with ACLs The Order of ACEs in an ACL
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.2 - The Order of ACEs in an ACL

## Slide 35: Processing Packet with ACLs The Order of ACEs in an ACL (cont.)
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.2 - The Order of ACEs in an ACL

## Slide 36: Processing Packet with ACLs Cisco IOS Reorders Standard ACLs
Notice that the statements are listed in a different order than they were entered.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.3 - Cisco IOS Reorders Standard ACLs

## Slide 37: Processing Packet with ACLs Cisco IOS Reorders Standard ACLs (cont.)
The order in which the standard ACEs are listed is the sequence used by the IOS to process the list.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.3 - Cisco IOS Reorders Standard ACLs (cont.)

## Slide 38: Processing Packet with ACLs Routing Processes and ACLs
As a frame enters an interface, the router checks to see whether the destination Layer 2 address matches its interface Layer 2 address, or whether the frame is a broadcast frame.
If the frame address is accepted, the frame information is stripped off and the router checks for an ACL on the inbound interface.
If an ACL exists, the packet is tested against the statements in the list.
If the packet matches a statement, the packet is either permitted or denied.
If the packet is accepted, it is then checked against routing table entries to determine the destination interface.
If a routing table entry exists for the destination, the packet is then switched to the outgoing interface, otherwise the packet is dropped.
Next, the router checks whether the outgoing interface has an ACL. If an ACL exists, the packet is tested against the statements in the list. If the packet matches a statement, it is either permitted or denied.
If there is no ACL or the packet is permitted, the packet is encapsulated in the new Layer 2 protocol and forwarded out the interface to the next device.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1 - Routing Processes and ACLs

## Slide 39: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 1
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.1 - Troubleshooting Standard IPv4 ACLs – Example 1

## Slide 40: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 1 (cont.)
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.1 - Troubleshooting Standard IPv4 ACLs – Example 1 (cont.)

## Slide 41: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 2
Security Policy: The 192.168.11.0/24 network should not be able to access the 192.168.10.0/24 network.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.2 - Troubleshooting Standard IPv4 ACLs – Example 2

## Slide 42: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 2 (cont.)
ACL 20 was applied to the wrong interface and in the wrong direction. All traffic from the 192.168.11.0/24 is denied inbound access through the G0/1 interface.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.2 - Troubleshooting Standard IPv4 ACLs – Example 2 (cont.)

## Slide 43: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 2 (cont.)
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.2 - Troubleshooting Standard IPv4 ACLs – Example 2 (cont.)

## Slide 44: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 3
Problem
Security Policy: Only PC1 is allowed SSH remote access to R1.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.3 - Troubleshooting Standard IPv4 ACLs – Example 3

## Slide 45: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 3 (cont.)
Solution!
Security Policy: Only PC1 is allowed SSH remote access to R1.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.3 - Troubleshooting Standard IPv4 ACLs – Example 3 (cont.)